## Slide 1: SAYAKA_AMR Notes
Xiaosong Sun
2018/05/28

## Slide 2: SAYAKA’s strategy: tree/block mixed AMR grid
Tree representation of refine levels
  Quad-tree (2D) and Oct-tree (3D)
  Tree node
    Parent node
    Leaf node
Block data in each tree node
  Uniform grid
  Refined by a factor of two each level

## Slide 3: Tree node
Faces x6 (or 2*ndim)
Children x8 (or 2^ndim)

## Slide 4: Tree level
Blocks with the same refinement
Level limits:
  Min level: static refine up to this level
  Max level: dynamic refine no over this level
  Finest level: current existing level the finest
  Possible range: [1, max level]
    NOTE beginning from 1 is designed
    Level 0 is left for future development

## Slide 5: Block data
Variable location
  Integer encoding the index type
  Cell: <0,0,0>
  Face: <1,0,0>, <0,1,0>, <0,0,1>
  Node: <1,1,1>
Index box
  Two integer vectors (low & high ends)
  Closed range of index
  Allows minus index

## Slide 6: Block data
Data buffer
  Valid part: true data
  Ghost part
    Data from neighbor block
    Data from coarser level
    Data from physical boundary
  Access by data(I,J,K,component)
  Staggered data may have overlap between two adjacent blocks -> need proper treatment

## Slide 7: Build a tree: root level

## Slide 8: Build a tree:

## Slide 9: Filling valid cell
Prolong
  Coarse -> Fine
  Injection
  Center difference
Restrict
  Fine -> Coarse
  Average
  Sum

## Slide 10: Filling ghost cell
Intra-level operations
  Fill block boundary on same level
  Fill physical boundary
Inter-level operations
  Fill coarse-fine boundary

## Slide 11: Concept of ‘Tower’
Set of uncovered blocks
  The highest tower is simply the collection of all leaf blocks
  The i-th tower is made by erasing top level of the (i+1)-th tower
What is tower for?
  Valid blocks need solving
  Manage coarse-fine face flux
  Natural multi-level grids

## Slide 12: MAC solver
Extensively use Tower
Only first-order at coarse/fine face
Can help compute flux of solution
MG precondition
  Levels of towers as multigrids
  GS as smoother, bottom use CG
CG solver

## Slide 13: Output and visualization
H5 Chombo file
  Paraview: choose *.h5 file -> select format “CHOMBO AMR file”
The HDF5-1.8.20 library is pre-compiled
If you wish, may also dump data to ASCII file in a level-by-level and block-by-block manner

## Slide 14: Helpful references
PARAMESH library
  Fortran code, the original idea of this tree/block model
  Unfortunately, project already obsolete, no longer maintained