## Slide 1: SAYAKA_AMR Notes
Xiaosong Sun
2018/05/28

## Slide 2: SAYAKA’s strategy: tree/block mixed AMR grid
Tree representation of refine levels
  Quad-tree (2D) and Oct-tree (3D)
  Tree node
    Parent node
    Leaf node
Block data in each tree node
  Uniform grid
  Refined by a factor of two each level

## Slide 3: Block data
Variable location
  Integer encoding the index type
  Cell: <0,0,0>
  Face: <1,0,0>, <0,1,0>, <0,0,1>
  Node: <1,1,1>
Index box
  Two integer vectors (low & high ends)
  Closed range of index
  Allows negative index

## Slide 4: Block data
Data buffer
  Valid part: true data
  Ghost part
    Data from neighbor block
    Data from coarser level
    Data from physical boundary
  Access by data(I,J,K,component)
  Staggered data may have overlap between two adjacent blocks -> need proper treatment

## Slide 5: Tree node
Faces x6 (or 2*ndim)
Children x8 (or 2^ndim)

## Slide 6: Tree level
Blocks with the same refinement
Fine level must be covered completely by its coarse level
Level limits:
  Min level: static refine up to this level
  Max level: dynamic refine no over this level
  Finest level: current existing level the finest
  Possible range: [1, max level]
    NOTE beginning from 1 is designed
    Level 0 is left for future development

## Slide 7: Build a tree: initialize root level
In general, the root level (level = 1) must be initialized by user.
Data to set
  Nodes number
  Domain length
  Boundary condition
  Node-to-node links
If the root level is rectangular, use the following easy method
  m_tree->initUniformRootLevel( { n0x,n0y,n0z }, // number of nodes probbox, // problem domain probbc, probperiodic); // BC type

## Slide 8: Build a tree: populate fine levels
The library will automatically manipulate the tree structure
The user should just specify “where to refine”

## Slide 9: Computation using SAYAKA
In most cases, the user can forget about the “tree”
Instead, one should focus on the block data on each node
  Just a (small, e.g. 8x8x8) Cartesian grid
  So the core algorithm keeps almost the same
What the library does for you?
  Synchronize data between fine and coarse levels -> data in valid cells
  Fill ghost cells for nodes on each level -> data in ghost cells

## Slide 10: Filling valid cell
Prolong
  Coarse -> Fine
  Direct injection
  Center difference
Restrict
  Fine -> Coarse
  Average
  Sum

## Slide 11: Filling ghost cell
Intra-level operations
  Fill block boundary on same level
  Fill physical boundary
Inter-level operations
  Fill coarse-fine boundary
Physical boundary
Same-level boundary
Coarse-fine boundary

## Slide 12: Concept of ‘Tower’
Set of uncovered blocks
  The highest tower is simply the collection of all leaf blocks
  The i-th tower is made by erasing top level of the (i+1)-th tower
What is tower for?
  Valid blocks need solving
  Manage coarse-fine face flux
  Natural multi-level grids

## Slide 13: MAC solver
Extensively use Tower
Only first-order at coarse/fine face
Can help compute flux of solution
MG precondition
  Levels of towers as multigrids
  GS as smoother, bottom use CG
CG solver
The MAC equation:
X: cell-centered unknown
a, b: scalar (e.g. time step)
A: cell-centered coefficient (e.g. pseudo-compressibility)
B: face-centered coefficient (e.g. reciprocal of density)

## Slide 14: Output and visualization
H5 Chombo file
  Paraview: choose *.h5 file -> select format “CHOMBO AMR file”
The HDF5-1.8.20 library is pre-compiled
If you wish, may also dump data to ASCII file in a level-by-level and block-by-block manner

## Slide 15: Examples
Test 7: time-dependent Stokes flow in an elbow channel.
This is a simple flow simulation without convection term.
Test 8: generate a function on the AMR tree and interpolate it to a simple grid.
This shows how to search data point in a tree.

## Slide 16: Helpful references
Download the newest code from my GitHub:
  https://github.com/haloless/SayakaAmr.git
  Remember to use VS2017
PARAMESH library
  Fortran code, the original idea of this tree/block model
  Unfortunately, project already obsolete, no longer maintained